## Slide 1: Agenda Item 8 – SMART Tracks
Speaker: Jason H, AIAL

## Slide 2: Agenda Item 8 – SMART Tracks Discussion – The Trial
    Three‑month trial, increasing the daily caps for northern SMART tracks RNP X and U (Yellow U23, Blue X05A and Green X23A)
    Commencing in autumn, over a five-month period
    Additional noise monitors will be deployed to best capture noise events
    Northern SMART track usage is not projected to rise in proportion to the cap increase

## Slide 3: What we know about SMART Tracks today
    SMART tracks use more precise flight paths.
    This improves efficiency, not only from airspace operations but fuel usage.
    It also means some corridors experience overflights more frequently.
    Engine thrust used less compared to STAR's
    SMART track utilisation can only occur when airspace conditions allow.
Current running average
AKL has approx. 220-240 landings per day, currently under 10% are utilising SMART tracks

## Slide 4: Northern SMART Track Utilisation During Trial (Forecast)
Below is Airways’ forecast for the busiest SMART track day once daily cap is increased:​
    Green track 13 each day (Current cap 10)​
    Blue track 10 each day (Current cap 10)​
    Yellow track 6 each day (Current cap 6)​
Running average is anticipated to be significantly lower than above figures.
If these numbers are reached, it will only be on days where conditions allow it, such as a low traffic day.

## Slide 5: impact
Marshall Day Acoustics – Assessment of Trial
Original caps were put in place to help understand potential noise effects.
Monitoring showed negligible community impact.
MDA predicts the increased use of the SMART tracks will reduce overall noise exposure (due to less noisy SMART descent profile)
Noise will increase for a small number of people that live directly below these tracks (due to precision and increased number of SMART approaches in that exact location)
MDA will carry out further numerical analysis and noise monitoring at select locations during the trial
Monitoring of the trial will be used to verify the initial MDA modeling

## Slide 6: A short-term trial to better understand community impact
    A 3-month trial of increased use of northern SMART approaches. (AKL and Airways have forecast that there will be many days with no increase).
    Designed to test:
    Changes in noise levels
    Changes in frequency of overflights
    Any change in complaints related to the northern SMART track utilisation
    What this may mean:
    Some areas may experience more overflights due to the SMART Track
    Other areas may experience less flights overhead
This trial is about understanding real-world impact — Before considering a permanent change